## Slide 1: Instability in Distributed Mobility Management
Yuanjie Li1, Haotian Deng2, Jiayao Li1, Chunyi Peng1, Songwu Lu1
1 University of California, Los Angeles
2 The Ohio State University
Notes:   (30s)
  Thanks for the introduction.
  In this talk, we will present a new structural property in cellular network’s mobility management.
  We will demonstrate the practical impact on mobile users, derive theoretical conditions for its satisfaction/violation, and present methods for its detection and resolution.

## Slide 2: Mobility Management is Ubiquitous and Critical
Ubiquitous network service to mobile users anytime, anywhere
Vital for data performance and seamless connectivity
Cellular Networks
Notes: The 3G/4G cellular network has become an essential part in our daily life.
It is the only large-scale infrastructure that provides “anywhere, anytime” mobile network service to users.
The key enabler is its mobility management, which determines the serving cell to the mobile device, and migrates the device to another as the device moves.
A good mobility management should provide seamless connectivity and high-speed data performance to users.

## Slide 3: One Fundamental Property for Mobility: Stability
Definition: given invariant condition (location, radio qualities, traffic, etc.), the mobile device eventually associate with a single cell
Impact of violation: persistent loop
  User-experienced performance downgrade
  Excessive signaling overhead to network operators
Instability ≠ Transient loops
  E.g., caused by radio dynamics and user movement
Cell 1
Cell 3
Cell 2
Notes: Emphasize the the stability differs from the radio link oscillations

## Slide 4: This Work: Instability in 3G/4G Mobile Network
Our focus: instability caused by mobility management plane
Q1: Does unstable mobility management exist in reality?
Q2: When shall instability happen?
Q3: How to detect and prevent instabilities?
Cell 1
Cell 3
Cell 2

## Slide 5
Unfortunately yes!
Q1: Does instability exist?

## Slide 6: How does 3G/4G Mobility Management work?
Mobility management via handoff
Configurable mobility management
  Tunable parameters and decision logic
Distributed mobility management
  Each cell maintains local parameters and decision logic
Cell 1
Cell 3
Cell 2
1
3
2
HO
decision
Movement
Meas
Cell | Pref
Cell 1 | 4
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | N/A
Cell 2 | 3
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
Notes: TODO: visualize these points. Minimize wording

## Slide 7: An Example of Unstable Handoff
Persistent loop: no convergence to single cell
  Under invariant setting: no radio oscillation, no mobility, stable traffic conditions, etc.
  Looped handoff every few minutes (90% loops <200s)
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Notes: TODO: visualize these points. Minimize wording

## Slide 8: Unstable Handoff Hurts both Users and Operators!
For users: performance downgrade
  10x slow down
For operators: signaling overhead
  2-8x over-the-air messages
12s
3s
76s
180s
Web latency
Video suspension
8.5x
3.5x
2.2x
Each handoff comes at a cost.
Persistent loops accumulate the costs!
Notes: TODO: visualize these points. Minimize wording

## Slide 9: Root Cause: Preference Configuration Inconsistency
Diverse demands, with different preferences
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Cell | Pref
Cell 1 | 4
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | N/A
Cell 2 | 3
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
  4GFemtocell: Femtocell is more preferred for traffic offloading
  Femtocell->3G: equal preference, but 3G’s radio quality is better
  3G->Femtocell: 4G is more preferred for higher-speed network service
Pref1,1< Pref1,2
Pref2,2= Pref2,3
Pref3,3< Pref3,1
Well-justified individual cell’s handoff policy
≠
Well-justified interplay between cells’ policies
Notes: TODO: visualize these points. Minimize wording

## Slide 10
Formulation, analysis and experimental validations
Q2: When shall instability happen?

## Slide 11: Formulation of Handoff Stability
Each handoff decision: s[t = Fs(C,P)]
  s, t: serving/target cell
  C: set of candidate cells (with runtime meas)
  P: configurable parameters
  Fs: decision logic (function) for serving cell s
Handoff sequences: sc1…  ci  [ci+1 = Fci (ci)] … t
Stability: for any invariant measurements, any handoff sequence always converge to a single cell t
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Notes: TODO: visualize these points. Minimize wording

## Slide 12: Causes of Instabilities: A Classification
Uncoordinated Parameter Configurations
Loop-prone handoff decision logics
BS 1
Cell 2
Pref1,1>Pref1,2
γ1<-105dBm, γ2>-110dBm
Pref2,1>Pref2,2
γ1>-108dBm
Inconsistent thresholds
Cell 1
Cell 2
Pref1,1<Pref1,2
γ2>-108dBm
Pref2,1=Pref2,2
γ1> γ2 +3dBm
Inconsistent preferences
BS 1
Cell 2
(Active)
γ1<-102dBm, γ2>-111dBm
(Idle) Pref2,1=Pref2,2
γ1> γ2 +3dBm
Active-idle misconfiguration
Cell 1
Cell 2
γ2>-106dBm
γ1>-106dBm
Active-state logic conflict
Cell 1
Cell 2
(Active)
Load balancing
(Idle) Pref2,1=Pref2,2
γ1> γ2 +3dBm
Active-idle logic conflict
Notes: Uncoordinated parameter:
Loop-prone decision logic: for whichever parameter used, the loop will always happen
- Briefly explain how conflicting decision logic can occur.
WARNING: at this moment idle/active handoff is not introduced yet.
Figures are too complex. Simplify them.
Be consistent with previous figures: shape, color, etc.

## Slide 13: Inconsistent Preferences: Instability Condition
These inconsistencies should always be avoided
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Cell | Pref
Cell 1 | 4
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | N/A
Cell 2 | 3
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
Proposition: persistent loop c1…  cn  c1 can always happen under some invariant measurements, if
  At least one cell ci configures Prefi,i < Prefi,i+1
  Every cell cj configures Prefj,j Prefj,j+1
Pref1,1< Pref1,2
Pref2,2= Pref2,3
Pref3,3< Pref3,1
Notes: TODO: visualize these points. Minimize wording

## Slide 14: Inconsistent Preferences: Empirical Validations
17 instances found in one U.S. operator
Diverse causes in reality
  4G-Femtocell-3G: uncoordinated handoff goals
  4G-Femtocell-2G-3G: device-side misconfiguration
  4G-4G: imprudent 4G infrastructure upgrade
c1 (4G, band 17)
c2 (4G, band 2)
c3 (4G, band 4)
c4 (Femtocell)
c5 (3G, band 850)
c6 (3G, band 1900)
c7 (2G)
Notes: TODO: visualize these points. Minimize wording

## Slide 15: Active-Idle Logic Conflict: Instability Condition
Idle-state logic is standardized
  Mandates the evaluation of cells’ radio quality
For stability, active-state decision logics must be regulated
Proposition: Two-cell persistent loop c1 c2 c1always exists, if c1’s active-state logic does not evaluate radio quality.
Cell 1
Cell 2
Idle-state logic: c2c1 iff.
Rss1> if Pref2,1>Pref2,2
Rss2>, Rss1> if Pref2,1>Pref2,2
Rss1> Rss2 if Pref2,1=Pref2,2
Notes: TODO: Re-plot the figures

## Slide 16: Active-Idle Logic Conflict: Empirical Validations
Found in two U.S. network operators
A design loophole in 3G Radio Resource Control (RRC) protocol
  Active-state handoff: no evaluation of radio quality
  Conflicts with idle-state handoff decision logic
Cell 1 (3G)
Cell 2 (3G)
RRC conn. release:
Redirect to cell 2
Rss1>Rss2
Reselect to cell 1
Notes: TODO: visualize these points. Minimize wording

## Slide 17
Persistent loop detection and fix guidelines
Q3: How to Detect and Prevent Instabilities?

## Slide 18: Persistent Loop Detection
Goal: uncover uncoordinated parameters and loop-prone logics
Approach: given parameters/logics, check (in)stability conditions
In-device implementation: help mobile device get rid of loops
Cellular Signaling Msg
(MobileInsight)
Decision Logic Inference
Configuration Collector
Instability Condition Checker
Counter
examples
Empirical
Validation
http://metro.cs.ucla.edu/mobile_insight/
Notes: TODO: Mention MobileInsight

## Slide 19: Persistent Loop Detection: Evaluation
Two major U.S. network operators
63 indoor locations, 50 outdoor locations
21 instances of instabilities detected, all observed in reality
Notes: TODO: visualize these points. Minimize wording

## Slide 20: Guideline for Instability Fix
Multiple fix schemes exist
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Cell | Pref
Cell 1 | 4
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | N/A
Cell 2 | 3
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
Pref1,1< Pref1,2
Pref2,2= Pref2,3
Pref3,3< Pref3,1
Notes: TODO: convert the wording to animations

## Slide 21: Guideline for Instability Fix
Multiple fix schemes exist
  Fix 1: on Cell 1, set Pref1,1> Pref1,2
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Cell | Pref
Cell 1 | 7
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | N/A
Cell 2 | 3
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
Pref1,1> Pref1,2
Pref2,2= Pref2,3
Pref3,3< Pref3,1
Notes: TODO: convert the wording to animations

## Slide 22: Guideline for Instability Fix
Multiple fix schemes exist
  Fix 1: on Cell 1, set Pref1,1> Pref1,2
  Fix 2: on Cell 2, set Pref2,2> Pref2,3
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Cell | Pref
Cell 1 | 4
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | N/A
Cell 2 | 4
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
Pref1,1< Pref1,2
Pref2,2> Pref2,3
Pref3,3< Pref3,1
Notes: TODO: convert the wording to animations

## Slide 23: Guideline for Instability Fix
Multiple fix schemes exist
  Fix 1: on Cell 1, set Pref1,1> Pref1,2
  Fix 2: on Cell 2, set Pref2,2> Pref2,3
But some fixes cause new loops
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Cell | Pref
Cell 1 | 4
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | N/A
Cell 2 | 3
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
Pref1,1< Pref1,2
Pref2,2= Pref2,3
Pref3,3< Pref3,1
Notes: TODO: convert the wording to animations

## Slide 24: Guideline for Instability Fix
Multiple fix schemes exist
  Fix 1: on Cell 1, set Pref1,1> Pref1,2
  Fix 2: on Cell 2, set Pref2,2> Pref2,3
But some fixes cause new loops
  Fix 3: on Cell 3, set Pref2,2< Pref2,1
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Cell | Pref
Cell 1 | 4
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | 4
Cell 2 | 3
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
Pref1,1< Pref1,2
Pref2,2= Pref2,3
Pref3,3< Pref3,1
Notes: TODO: convert the wording to animations

## Slide 25: Guideline for Instability Fix
Multiple fix schemes exist
  Fix 1: on Cell 1, set Pref1,1> Pref1,2
  Fix 2: on Cell 2, set Pref2,2> Pref2,3
But some fixes cause new loops
  Fix 3: on Cell 3, set Pref2,2< Pref2,1
  New loop: c1c3c1
Cell 1 (4G)
Cell 3 (3G)
Cell 2
(Femtocell)
Cell | Pref
Cell 1 | 4
Cell 2 | 6
Cell 3 | 3
Cell | Pref
Cell 1 | 4
Cell 2 | 3
Cell 3 | 3
Cell | Pref
Cell 1 | 5
Cell 2 | 3
Cell 3 | 3
Pref1,1< Pref1,2
Pref2,2= Pref2,3
Pref3,3< Pref3,1
Guideline (monotonic fix): for any meas that cannot trigger cicj before applying the fix scheme, it should not trigger cicj after the fix
Notes: TODO: convert the wording to animations

## Slide 26: Conclusion
Instability exists in mobility management plane
  Distributed management in nature
  Negative impact: performance degradation, signaling overhead
Instability can be prevented with coordination of mobility management
  Regulation of parameters and decision logics are necessary
More aspects of mobility management remain open research areas
  More structural properties: reachability, security, consistency, etc.

## Slide 27: Thank you!

## Slide 28: Backup

## Slide 29: Details of the Instability Conditions