## Slide 1: Supporting Mobile VR in LTE Networks: How Close are We?
Zhaowei Tan, Yuanjie Li, Qianru Li,
Zhehui Zhang, Zhehan Li, Songwu Lu

## Slide 2: Booming Virtual Reality Market
We witness a boom in Virtual Reality (VR)
$4.9B Revenue in 2017
21M hardware sold in 2017
Projected $40B Market by 2020
(Source: Orbit Research & Superdata Research)

## Slide 3: Mobile Virtual Reality
Units Sold Until 2018
8M
10M
Samsung
Gear VR
Google
Cardboard
Advantages of Mobile VR
Affordable price
($20-$100 per unit)
Excellent convenience
(No wiring required)

## Slide 4: Users’ Demand for Mobile VR
Anywhere, anytime
(outdoor/indoor, static/mobile)
High fidelity
(≥1080p, ≥60FPS, low latency)
1. User Pose
(from sensors)
2. Graphical
Processing
3. Frame
Transfer
4. Display
Edge-based Scheme over Mobile Networks

## Slide 5: Mobile VR over LTE Network
4G LTE:
The largest mobile network infrastructure for “anywhere, anytime” Internet services
2. Graphical
Processing
3. Frame
Transfer
4. Display
LTE
1. User Pose
(from sensors)
Edge-based Scheme over Mobile Networks

## Slide 6: How LTE Network Works
2. Graphical
Processing
3. Frame
Transfer
4. Display
Core
1. User Pose
(from sensors)
Radio

## Slide 7: How LTE Network Works
Link Layer
Physical Layer
Control Signaling
Control Signaling
Media Access Control
Radio Link Control
Link layer
{
Radio Resource Control

## Slide 8: Can LTE Support Mobile VR?
Key Challenge: Network Latency
For human tolerance: Should not exceed 25ms
This talk:
  Does 4G LTE have the potential to enable VR?
  What are the roadblocks for mobile VR over LTE?
  What are the possible solutions to the roadblocks?

## Slide 9: 1. Does LTE have the potential?

## Slide 10: A First Look at VR over LTE
  LTE exhibits signs to meet latency requirement for medium quality VR
  User regularly experiences long latency

## Slide 11: 2. What are the roadblocks?

## Slide 12: Analysis Methodology
LTE
8-month empirical study
Verizon, AT&T, T-Mobile, Sprint
3M LTE messages+21M packets
“Black-box”
Identify latency deficiencies
Derive equations for latency
Challenge: LTE is a closed “black-box” system
Our approach:
Standard Analysis
Device-Side Empirical Study

## Slide 13: Five Intuitions for VR over LTE
  Wireless bandwidth is the bottleneck for VR
  LTE can quickly recover wireless data corruption
  Device receives new data immediately after handover
  Uplink motions are quickly sent to the base station
  Handover in LTE incurs unnoticeable latency

## Slide 14: Five Intuitions for VR over LTE
  Wireless bandwidth is the bottleneck for VR.
  LTE can quickly recover wireless data corruption
  Device receives new data immediately after handover
  Uplink motions are quickly sent to the base station
  Handover in LTE incurs unnoticeable latency
We invalidate all of them!

## Slide 15: Overview of Findings
  Wireless bandwidth is the bottleneck for VR.
  LTE can quickly recover wireless data corruption
  Device receives new data immediately after handover
  Uplink motions are quickly sent to the base station
  Handover in LTE incurs unnoticeable latency
Sufficient bandwidth for medium quality VR
LTE signaling operations contribute a bulk portion of latency
Inter-protocol incoordination
Single-protocol deficiency

## Slide 16: Sufficient Bandwidth for Medium-Quality VR
Uplink
Misunderstanding:
Wireless bandwidth is the bottleneck for VR.
Reality: Sufficient LTE bandwidth for mobile VR!
Insight: Simply improving bandwidth is not enough
Downlink
Bandwidth
Inter-Protocol
Single-Protocol

## Slide 17: Inter-Protocol Incoordination: Head-of-Line Blocking in Mobility
Misunderstanding:
Device receives new data immediately after handover
Reality: Duplicate data incurs head-of-line blocking!
61% – 92% handover incurs head-of-line blocking
30.0 – 44.7ms head-of-line blocking latency
80ms at maximum
Bandwidth
Inter-Protocol
Single-Protocol

## Slide 18: Inter-Protocol Incoordination: Head-of-Line Blocking in Mobility
ACK
Bandwidth
Inter-Protocol
Single-Protocol
Root Cause: Problematic interplay between radio link control and radio resource control
Insight: Radio link control should be handover friendly for mobile VR

## Slide 19: Single-Protocol Deficiency: Latency-Unfriendly Control Channel
Misunderstanding:
The user motion will be quickly sent out to the edge
Reality: 81% uplink packets perceive 6-9ms extra delay!
Bandwidth
Inter-Protocol
Single-Protocol

## Slide 20: Single-Protocol Deficiency: Latency-Unfriendly Control Channel
Scheduling request
Radio grant
Data transmission
Bandwidth
Inter-Protocol
Single-Protocol
Root Cause: Scheduling-based latency-unfriendly uplink control channel protocol design

## Slide 21: Single-Protocol Deficiency: Latency-Unfriendly Control Channel
Fundamental tradeoff between
resource utilization and uplink latency
Bandwidth
Inter-Protocol
Single-Protocol
Root Cause: Scheduling-based latency-unfriendly uplink control channel protocol design

## Slide 22: Single-Protocol Deficiency: Latency-Unfriendly Control Channel
Insight: The general latency-utilization tradeoff can be bypassed by periodic VR traffic
Periodic VR uplink traffic
Bandwidth
Inter-Protocol
Single-Protocol
Root Cause: Scheduling-based latency-unfriendly uplink control channel protocol design

## Slide 23: Summary: How Problems Happen
Problematic and slow signaling protocol interplays
  Well-designed single protocol ≠ Proper protocol interplays
Extra delays from each protocol’s signaling actions
  Unnoticeable in general, but critical for mobile VR
The LTE network protocols are unaware of mobile VR’s traffic patterns

## Slide 24: 3. What are the solutions?

## Slide 25: LTE-VR: LTE Booster for Mobile VR
A device-centric approach
  Only the device side has enough message
  No expensive infrastructure side update
Mobile Phone
Client Side
Cross-layer design
Side-channel info
Masking intra-protocol latency
Mitigating inter-protocol latency

## Slide 26
ACK
ACK
ACK
Mitigate Head-of-Line Blocking
Inter-Protocol
Single-Protocol
Strawman solution: Immediately acknowledge every received VR data
Challenge: Excessive signaling messages
ACK
ACK
ACK
ACK
ACK
ACK
ACK

## Slide 27
ACK
Mitigate Head-of-Line Blocking
ACK
ACK
ACK
ACK
ACK
Strawman solution: Immediately acknowledge every received VR data
Challenge: Excessive signaling messages
Solution:
Selective feedback using handover prediction
Inter-Protocol
Single-Protocol
Measurement:
RSSIbs2>RSSIbs1
Prediction:
Handover to BS2

## Slide 28: Mask Uplink Control Latency
Strawman: Allocate resource before VR data arrives
Challenge: Potential resource waste
Scheduling request
Radio grant
Data transmission
Scheduling request
Radio grant
Data transmission
Wasted
Inter-Protocol
Single-Protocol

## Slide 29: Mask Uplink Control Latency
Strawman: Allocate resource before VR data arrives
Challenge: Potential resource waste
VR traffic arrival prediction
Solution:
Proactive allocation using VR traffic prediction
Scheduling request
Radio grant
Data transmission
Inter-Protocol
Single-Protocol

## Slide 30: Implementation and Prototype
Software implementation in device radio firmware
  No hardware modification
Approximative prototype with OpenAirInterface and Universal Software Radio Peripheral (USRP)
  Firmware not open-sourced to academia

## Slide 31: Evaluation
Can LTE-VR meet mobile VR’s latency demands?
How much overhead does LTE-VR occur?
Can LTE-VR be used in 5G?

## Slide 32: Can LTE-VR Meet VR’s Demands?
Yes: Meet delay tolerance with 95% probability
  Reduce latency outlier frames by 3.7x
Approximate oracle LTE
Comparable to 10x bandwidth expansion

## Slide 33: How Much is the Overhead?
4% - 8% signaling messages
0.1% downlink throughput
2.3% extra uplink grants
Negligible overhead!
LTE-VR leverages phone-side information to reduce the overhead as much as possible

## Slide 34: Can LTE-VR be Used in 5G?
Yes!
Complimentary to existing 5G radio technologies*
  Up to 31x improvement on latency outliers
Provides insights on 5G signaling design
  Most 5G signaling designs so far inherits 4G counterparts
Applicable to other latency-sensitive apps
  Augmented reality, autonomous driving, gaming, …

## Slide 35: Summary
LTE is promising for mobile VR, but not perfect
  High bandwidth ≠ low latency
  This work: Demystify 5 misunderstandings
LTE-VR: An in-device LTE booster for mobile VR
  Only the device has the info for VR latency reduction
Still a long voyage toward ultra-low latency 5G

## Slide 36: Thank you! For code and dataset: http://metro.cs.ucla.edu/mobileVR.html